## Slide 1: EMBEDDED Systems RELIABILITY
SAFE FSM ENCODING – LAB EXERCISE
Dimitrios agiakatsikas, Mihalis Psarakis

## Slide 2: Finite state machine (fsm) – binary encoding
Example1:
  8 states: s0 to s7
  Binary encoding
    000 (s0), 001 (s1), …, 111 (s7)
  One state (s3) is not used
constant s0 : std_logic_vector(N-1 downto 0) := "000";
constant s1 : std_logic_vector(N-1 downto 0) := "001";
constant s2 : std_logic_vector(N-1 downto 0) := "010";
constant s3 : std_logic_vector(N-1 downto 0) := "011";
constant s4 : std_logic_vector(N-1 downto 0) := "100";
constant s5 : std_logic_vector(N-1 downto 0) := "101";
constant s6 : std_logic_vector(N-1 downto 0) := "110";
constant s7 : std_logic_vector(N-1 downto 0) := "111";
s5
s6
s7
s3
s0
s2
s4
s1
Unused (invalid) state
-- State sequence: s0-s1-s2-s4-s5-s6-s7-s0-...
-- S3 state is unused (invalid)
next_state <= s3 when current_state = s3 else
s4 when current_state = s2 else
current_state + "001";
FSM hang

## Slide 3: FSM - Fault injection platform
-- Instantiate the frequency divider
freq_div_u:
entity work.freq_div(Behavioral)
generic map(CLK_INPUT => 125000000,
CLK_OUTPUT => 1)
port map(clk_in => clk,
clk_out => clk_1Hz);
-- Instantiate the Pulse Generator for the "error_inject" signal
pulse_gen_u:
entity work.pulse_gen(Behavioral)
port map(clk => clk_1Hz,
pulse_in => error_inject,
pulse_out => error_inject_p
);
-- !!!!!!!!!!!!!!! Instantiate the Target FSM !!!!!!!!!!!!!!
-- Options: FSM (Binary), FSM_Onehot, FSM_Hamming3
FSM_u:
entity work.FSM(Behavioral)
generic map(N => N)
port map(rst => rst,
clk => clk_1Hz,
play => play,
state_out => state_out(N-1 downto 0),
error_inject => error_inject_p,
error_data => error_data,
alarm => alarm
);
FSM
rst
(bt0)
clk_1Hz
play
(sw3)
Freq divider
clk
pulse gen
error_inject
(sw2)
error_data (sw1:0)
state_out
Pmod JD (Led 7:0)
alarm
RGB Led

## Slide 4: FSM - Fault injection platform
-- State sequence: s0-s1-s2-s4-s5-s6-s7-s0-...
-- S3 state is unused (invalid)
next_state <= current_state when current_state = s3 else
s4 when current_state = s2 else
current_state + "001";
process(rst, clk)
begin
if rst = '1' then
current_state <= s0;
elsif rising_edge(clk) then
if play = '1' then
current_state <= next_state;
elsif error_inject = '1' then
current_state(1 downto 0) <= current_state(1 downto 0) XOR error_data;
end if;
end if;
end process;
state_out <= current_state;
alarm <= '1' when (current_state = "011") else -- Invalid state
'0';
FSM
rst
(bt0)
clk_1Hz
play
(sw3)
Freq divider
clk
pulse gen
error_inject
(sw2)
error_data (sw1:0)
state_out
Pmod JD (Led 7:0)
alarm
RGB Led
Alarm when invalid state

## Slide 5: Finite state machine (fsm) – SAFE DESIGN
Example:
  8 states: s0 to s7
  Binary encoding
    000 (s0), 001 (s1), …, 111 (s7)
  One state (s3) is not used
Safe FSM:
  Reset the FSM when an invalid state occurs
constant s0 : std_logic_vector(N-1 downto 0) := "000";
constant s1 : std_logic_vector(N-1 downto 0) := "001";
constant s2 : std_logic_vector(N-1 downto 0) := "010";
constant s3 : std_logic_vector(N-1 downto 0) := "011";
constant s4 : std_logic_vector(N-1 downto 0) := "100";
constant s5 : std_logic_vector(N-1 downto 0) := "101";
constant s6 : std_logic_vector(N-1 downto 0) := "110";
constant s7 : std_logic_vector(N-1 downto 0) := "111";
s5
s6
s7
s3
s0
s2
s4
s1
Unused (invalid) state
-- State sequence: s0-s1-s2-s4-s5-s6-s7-s0-...
-- S3 state is unused (invalid)
next_state <= s0 when current_state = s3 else
s4 when current_state = s2 else
current_state + "001";
Return to reset state

## Slide 6: Finite state machine (fsm) – one-hot encoding
Example2:
  8 states: s0 to s7
  One-hot encoding
    00000001 (s0), 00000010 (s1), …, 10000000 (s7)
  8 valid states
    248 invalid states
constant s0 : std_logic_vector(N-1 downto 0) := "00000001";
constant s1 : std_logic_vector(N-1 downto 0) := "00000010";
constant s2 : std_logic_vector(N-1 downto 0) := "00000100";
constant s3 : std_logic_vector(N-1 downto 0) := "00001000";
constant s4 : std_logic_vector(N-1 downto 0) := "00010000";
constant s5 : std_logic_vector(N-1 downto 0) := "00100000";
constant s6 : std_logic_vector(N-1 downto 0) := "01000000";
constant s7 : std_logic_vector(N-1 downto 0) := "10000000";
-- State sequence: s0-s1-s2-s3-s4-s5-s6-s7-s0-...
next_state(N-1 downto 1) <= current_state(N-2 downto 0);
next_state(0) <= current_state(N-1);

## Slide 7: Finite state machine (fsm) – one-hot encoding
Example2:
  8 states: s0 to s7
  One-hot encoding
    00000001 (s0), 00000010 (s1), …, 10000000 (s7)
  8 valid states
    248 invalid states
Safe FSM:
  Detect (and alarm) the invalid states
process(current_state)
variable count1s : integer range 0 to N;
begin
count1s := 0;
for i in 0 to N-1 loop
if current_state(i) = '1' then
count1s := count1s + 1;
end if;
end loop;
if count1s = 1 then
alarm <= '0';
else
alarm <= '1';
end if;
end process;

## Slide 8: Finite state machine (fsm) – hamming-3 coding
Example2:
  8 states: s0 to s7
  Binary encoding
    000 (s0), 001 (s1), …, 111 (s7)
constant s0 : std_logic_vector(2 downto 0) := "000";
constant s1 : std_logic_vector(2 downto 0) := "001";
constant s2 : std_logic_vector(2 downto 0) := "010";
constant s3 : std_logic_vector(2 downto 0) := "011";
constant s4 : std_logic_vector(2 downto 0) := "100";
constant s5 : std_logic_vector(2 downto 0) := "101";
constant s6 : std_logic_vector(2 downto 0) := "110";
constant s7 : std_logic_vector(2 downto 0) := "111";
…
process(rst, clk)
begin
if rst = '1' then
current_state <= s0;
elsif rising_edge(clk) then
if play = '1' then
current_state <= next_state;
elsif error_inject = '1' then
current_state(1 downto 0) <= current_state(1 downto 0) XOR error_data;
end if;
end if;
end process;
-- State sequence: s0-s1-s2-s3-s4-s5-s6-s7-s0-...
next_state <= current_state + "001";

## Slide 9: Finite state machine (fsm) – hamming-3 coding
Example2:
  8 states: s0 to s7
  Binary encoding
    000 (s0), 001 (s1), …, 111 (s7)
Safe FSM:
  Detect (and alarm) and correct the invalid states
process(rst, clk)
begin
if rst = '1' then
current_state <= s0;
p <= (others => '0');
elsif rising_edge(clk) then
if play = '1' then
current_state <= next_state;
p(0) <= next_state(0) XOR next_state(1);
p(1) <= next_state(0) XOR next_state(2);
p(2) <= next_state(1) XOR next_state(2);
elsif error_inject = '1' then
current_state(1 downto 0) <= current_state(1 downto 0)
XOR error_data;
end if;
end if;
end process;
state_out <= current_state & p;
alarm <= '1' when (s /= "000") else
'0';
s(0) <= current_state(0) XOR current_state(1) XOR p(0);
s(1) <= current_state(0) XOR current_state(2) XOR p(1);
s(2) <= current_state(1) XOR current_state(2) XOR p(2);
current_state_corr <= current_state XOR "001" when s = "011" else
current_state XOR "010" when s = "101" else
current_state XOR "100" when s = "110" else
current_state;
next_state <= current_state_corr + "001";
Κατάσταση | Σφάλματα στα bit ισοτιμίας | Σύνδρομο
No error | None | 0 0 0
Bit 1 (p0) error | p0 | 0 0 1
Bit 2 (p1) error | p1 | 0 1 0
Bit 3 (p2) error | p2 | 1 0 0
Bit 4 (s0) error | p0, p1 | 0 1 1
Bit 5 (s1) error | p0, p2 | 1 0 1
Bit 6 (s2) error | p1, p2 | 1 1 0