## Slide 2: Εξέλιξη Συστημάτων Κινητών Επικοινωνιών
Wide area coverage
TDMA
CDPD
43.2 Kbps
GSM HSCSD
115.2 Kbps
PDC/PDCP
14.4 Kbps
cdmaOne
(IS-41)
76.8 Kbps
EDGE
384 Kbps
GPRS
170 Kbps
GERAN
475 Kbps
WCDMA FDD
2 Mbps
WCDMA TDD
2 Mbps
WCDMA HSPDA
10 Mbps
Downlink
EDGE Upgrades
2 Mbps
TD-SCDMA
2 Mbps
cdma2000 1X
308 Kbps
cdma2000 1XEV-DO
2.4 Mbps
cdma2000 1XEV-DV
5.4 Mbps
IEEE 802.11a
6-54 Mbps
IEEE 802.11b
1-11 Mbps
HiperLAN
II
54 Mbps
OFDM at the 5-6 GHz U-NII
3G Evolution
Higher data rate WLAN
(100 Mbps)
Harmonization
Local area coverage
3G
2G
4G
Future wireless systems
LTE
5G
4G+
LTE-A
LTE-A Pro
LTE-V2X
IEEE 802.16e
WiMAX
IEEE 802.16m
WiMAX
UMTS
IEEE 802.11ac
IEEE 802.11ax
IEEE 802.11p
___________________________________________________________________________________________________________________________________________

## Slide 3: Fundamental Multiple Access methods
FDMA
  Frequency division multiple access
TDMA
  Time division multiple access
CDMA
  Code division multiple access
ALOHA
  satellite
802.11
  CSMA/CA
  OFDMA
Notes: FDMA – brukere får allokert forskjellige bærebølge frekvenser av tilgjengelig radio spektrum
TDMA – brukere kan dele samme frekvens ved å dele frekvensen opp i tidslotter.
CDMA – deler ikke kanalen i frekvens eller tid, men koder dataen som blir sendt

## Slide 4: What is 802.11?
Suitable for indoor/local wireless coverage
  Typical range under 50 meters
  Range highly dependent on the space layout
Optimized for packet based communication, e.g., Internet Protocol (IP)
Transmission speed
  Up to 11 Mbps for 802.11b
  Up to 54 Mbps for 802.11a or 802.11g

## Slide 5: 802.11 is an Open Technology
Anyone can build and sell WLAN equipment as long as
  Power radiation regulations are obeyed
Interoperability standards are mature and openly available (IEEE 802.11 and WiFi Alliance)
No need for spectrum license to operate WLAN
  WLAN operates in 2.4 GHz (b, g) or 5 GHz (a) unlicensed bands
Openness of technology is a blessing as well as a liability!
  Compare Internet with telephone (fixed and mobile) networks

## Slide 6: WLAN Already a Commodity
Variety of WLAN equipment is already available in the marketplace
  Access point, PCIMCA cards for laptops, bridges for desktops
  WLAN built in laptops, PDAs, Mobile phones
  WLAN chipsets
  WLAN related softwares
WLAN available for enterprise, domestic and public applications

## Slide 7: Why use WLAN?
WLANs are an alternative to high installations and maintenance cost which is experienced with traditional LAN infrastructures.
Physical and environmental necessity is a driving factor in favor of WLAN
  buildings which are difficult or impossible to wire:
    Ex.: warehouses, campus and historical buildings
WLAN is better then LAN when networks are only temporarily:
  Ad hoc networking
    Emergency centers
    Tactical military environments (sensor networks)
Notes: Hvorfor bruke trådløse lokalnett
Trådløse nettverk er et alternativ til store installasjoner og høye vedlikeholds kostnader som vi har erfart ved tradsjonelle lokalnettverk.
Fysiske og miljømessige spørsmål er en drivende faktor i favør av WLAN
  F.eks så kan bygninger være vanskelig å kable
    Da warehouses, campus eller historiske bygninger
Trådløse nettverk er bedre enn kablede LAN når når nettverk er satt opp for en midlertidlig periode:
  Da f.eks ad hoc nettverking
    I et krisesentere
    Taktiske militære områder, altså sensor nettverk

## Slide 8: WLAN Network Architecture (1/2)
Basic Service Set (BSS): a set of stations which communicate with one another
Ad hoc network
Only direct communication possible
No relay function
Infrastructure Mode
Stations communicate with AP
AP provides connection to wired network (e.g. Ethernet)
Stations not allowed to communicate directly

## Slide 9: WLAN Network Architecture (2/2)
ESS: a set of BSSs interconnected by a distribution system (DS)
Local Area Network (e.g .Ethernet)

## Slide 10: 802.11 Terminologies
BSS: Basic service set
  Group of stations under the direct control of a single co-ordination function
  All stations in a BSS can directly communicate with each other, without any infrastructure
  Geographical area covered by BSS is BS Area
  BSA is similar in concept to a ‘cell’ in a cellular network

## Slide 11: 802.11 Terminologies
Access Point (AP):
  Similar to the base station in cellular network
  Supports range extension by providing network connectivity between multiple BSSs
  Multiple BSSs are connected together through a Distribution System (DS)
  DS is similar to a backbone network
  BSSs connected by a DS form an Extended Service Set (ESS)

## Slide 12: Infrastructure Networks
Two advantages for infrastructure networks
  The mobile stations need not to maintain neighbor relationships.
  Access points assist with stations attempting to save power.
In an infrastructure network, stations must associate with an AP to obtain network services. (equivalent to plug in the network cable)
An extended service set (ESS) is created by chaining BSSs together with a backbone network.

## Slide 13: Typical Connection Procedure
1) Authentication exchange
2) Association exchange
3) Encrypted data exchange
Client proves its identity to AP
Client binds its identity to AP
Data communication may continue

## Slide 14: WLAN Fundamental Standards
Standard | 802.11 | 802.11a | 802.11b | 802.11g
Year | 1997 | 1999 | 1999 | 2001
Freq | 2.4 GHz | 5 GHz | 2.4 GHz | 2.4 GHz
Speed | 2 Mbps | 54 Mbps | 11 Mbps | 54 Mbps
Modulation | FHSS / DPSK | OFDM /QAM | DSSS/ CCK | OFDM / CCK
Distance | 100 m | 30 m | 100 m | 100 m

## Slide 15: 802.11 task forces
802.11a
  New physical layer using 5 GHz band utilizing Orthogonal Frequency-Division Multiplexing (OFDM) to provide speeds up to 54 Mbps
  Lower range and higher power requirements
802.11b
  Existing implementation using 2.4 GHz band to provide speeds up to 11 Mbps
  High range and low power requirements
802.11d
  AP specifies a client profile which includes channel set and power
  Allows for single AP and client product which would self-configure to meet local RF regulations
  International roaming – “World Mode”
802.11e
  Quality of Service (QoS) support
  Coupled with 802.1p (Class of Service) and 802.1q
  Support for real-time applications like voice and streaming media
  Dynamically-plumbed WEP keys
Notes: The Future of WLAN Technology
  For more information on existing and emerging standards, visit http://grouper.ieee.org/groups/802/11/
  802.11d will enable a WLAN client adapter to be auto-configured by the AP with which it connects.
  QoS, available in 802.11e, will allow the tagging of packets coming from a particular source or application type as a higher priority, thus increasing the rate at which these TCP/IP data packets are delivered and read. This is of great benefit to such technologies as streaming media and voice over IP.

## Slide 16: 802.11 task forces
802.11f
  Seamless handoffs between access points
802.11g
  New physical layer using 2.4 GHz band utilizing OFDM
  Max speed 22 Mbps, but cannot coexist with 802.11b
802.11h
  Enhancement to MAC to support EU power and RF requirements
  Recommended feature for any future implementations
802.11i
  Enhanced security
  Advanced Encryption Standard (AES) strong contender for replacing WEP
  May be used with 802.1X
Notes: The Future of WLAN Technology
  802.11h offers changes to the MAC layer for 802.11 which will allow a more dynamic control for transmit power and frequency settings.
  802.11i is an enhancement to security for 802.11. Instead of using WEP, 802.11i will use a new technology called Advanced Encryption Standard (AES). 802.1X is an interim solution, whereas 802.11i is the final, formal solution.
  802.11q provides support for virtual LANs (VLANs) within a bridge or switch. Consider that the AP is a switch. With 802.1X, if a user is authenticated, the user gets a corporate LAN connection, which also provides a connection to the Internet. Currently, however, if the authentication fails, the user does not get connected to anything. 802.11q will enable the user, such as a visiting business partner who does not have valid corporate network credentials, to at least receive a fail-over connection to the Internet when corporate network authentication fails.

## Slide 17: 802.11 task forces
802.11j
  The 802.11j Task Group is working on Japanese regulatory extensions to allow for operation in the 4.9 GHz and 5GHz bands in Japan. This is expected to be approved in 2005.
802.11k
  802.11k is focused on standardizing the radio measurements that will allow uniform measurement of radio information across different manufacturer platforms.
  By having standardized, repeatable measurements, system designers can utilize radio environment information to make better decisions as to frequency use, transmit power levels, etc.
802.11n
  The 802.11n Task Group is focusing on creating a standard to further increase the net throughput of wireless networks.
  The goal is to achieve greater than 150 Mbps usable throughput over an 802.11.
  Both physical and MAC layer changes are being considered, but backward compatibility is required.

## Slide 18: 802.11 task forces
802.11r
  The 802.11r Task Group is working on reducing the handoff latency when client devices transition between access points or cells in an ESS.
  This standard will facilitate the deployment of SIP-based Voice over Wi-Fi (VoWi-Fi) portable phones.
802.11s
  The 802.11s Task Group is working on an infrastructure mesh standard to allow 802.11 access points or cells from multiple manufacturers to self-configure into multi-hop wireless topologies.
  Example usage scenarios for mesh networks include interconnectivity for devices in the digital home, unwired campuses, and community area networks or hotzones.

## Slide 19: 802.11 task forces
802.11p
  Wireless Access for Vehicular Environment (WAVE).
  Dedicated short-range communications (DSRC) frequencies are used.
  The concept of Road Side Units (RSUs) is applied.

## Slide 20: 802.11 task forces
Multiple 802.11 standards can coexist

## Slide 21: 802.11 Generations
Regarding the design of MAC & Physical layers

## Slide 22: Enhancing 5G indoor infrastructures

## Slide 23: WiFi 5 vs WiFi 6: What is the difference?

## Slide 24: WLAN Characteristics - Frequency Bands
802.11a Wireless LAN
802.11b Wireless LAN
Bluetooth
Cordless Phone
GSM Handphone

## Slide 25: WLAN Protocol Stack
OFDM
PHY
PHY – Converts signals from the MAC Layer to Radio Signals
MAC – Implements the CSMA / CA Mechanism
LLC – Provides Interface to upper Layers

## Slide 26: WLAN Technical – Physical Layer
Transmission Method
  Spread spectrum (DSSS) for 11 Mbps 802.11b in 2.4 GHz band
  Orthogonal frequency division multiplexing (OFDM) for 54 Mbps 802.11g in 5 GHz band
  OFDM for 54 Mbps 802.11a in 5 GHz band

## Slide 27: Radio technology
IEEE 802.11 provides for two variations of the PHY using RF technology:
  Direct Sequence Spread Spectrum (DSSS)
  Frequency Hopped Spread Spectrum (FHSS)
The DSSS and FHSS PHY options is designed for operations in the 2.4 GHz ISM band.
Two new techniques were introduced to achieve higher bandwidth:
  Orthogonal Frequency Division Multiplexing (OFDM) modulation and High Rate – DSSS with transmission rates >=54 Mbps and >=11 Mbps, respectively.

## Slide 28: Channel bandwidth for DSSS
802.11b with DSSS has a available throughput-capacity of 11 Mbps/channel
Divides spectrum in 3 channels to reduce co-channel interference.
The channel bandwidth is 22 MHz for DSSS systems.
Notes: DSSS benytter 3 kanaler i 2.4 GHz båndet.
Hver kanal har da en overførings-kapasitet på 11 Mbps i 802.11b.
Radiospekteret er oppdelt i 3 kanaler for å minske interferens mellom kanaler.
Båndbredden for hver kanal er da 22 MHz

## Slide 29: Frequency Hopped Spread Spectrum (FHSS)
FHSS is a spread-spectrum method of transmitting radio signals by rapidly switching a carrier among many frequency channels, using a pseudorandom sequence known to both transmitter and receiver.
High effect in a narrow frequency band (1 MHz = 1 Channel)
Different hopping sequences enables multiple BSS to coexist in the same geographical area.
  Alleviate congestion and maximize total throughput in BSS
Currently used in Bluetooth.
Notes: Frekvens hoppende spread spektrum
  Teknikk for å overføre radio-signaler ved å bytte bærebølge mellom flere frekvens-kanaler
FHSS sender ut høy effekt i en liten del av frekvensbåndet
Forskjellige hoppesekvenser muliggjør at flere BSSs kan operere i samme område
Brukes nå bare i bluetooth

## Slide 30: Medium Access Control (MAC) Layer
Manages access of multiple wireless stations to shared wireless medium.
  CSMA/CA (Carrier Sense Multiple Access with Collision Avoidance)
Assists in security over the wireless link
  Encrypt all wireless communication
  Authenticate clients before granting access
Assists in association management
  Binding client identity of access point
  Portability, mobility

## Slide 31: Medium Access Control (MAC) Layer
Activities:
  Channel allocation procedures
  Protocol Data Unit (PDU) addressing
  Frame formatting
  Error checking
  Fragmentation and reassembly
Medium alternates between two modes:
  Contention Period (CP)
  Contention Free Period (CFP)
Notes: Medium Access Control sublaget har ansvaret for
Prosedyrer for å allokere kanaler. Situasjonen her blir litt annerledes når vi opererer trådløst enn i ether.
Addressering av protocol data units
Formaterring av rammer
Feilsjekking av MPDU
Fragmentering og reassembleringav pakker
Aksess mediet kan befinne seg i 2 tilstander
Contention period
Contention free period
Mediet kan operere eksklusivt i konkurranse-modus. Da må alle nodene konkurrere om aksess til kanalen for hver pakke som skal sendes.

## Slide 32: 802.11 MAC Frames
Management Frames: Used for
  Station association, dissociation, timing and synchronization, authentication
Control Frames: Used for
  Handshaking during CP (RTS/CTS)
  ACK frames during CP
Data Frames: Used for
  Sending data during CP and CFP

## Slide 33: 802.11 frame format
IEEE 802.11 support three types of frames:
Management frames: station association and disassociation with AP, timing and sychronization, authentication and deauthentication.
Control frames: handshaking and ack during CP, and to end the CFP
Data frames: transmission of data, can be combined with polling and acknowledgements
Notes: IEEE 802.11 tilbyr tre typer frames.
Vi har management-frames som brukes for å assosiere en stasjon med et aksesspunkt. Og for deassosiering. Brukes for tids-styring og synkronisering, samt autentisering og deautentisering.
Kontroll frames brukes for handshaking under Konkurranse Perioden, samt positive acknowledgements. De brukes også ved avslutning av en en konkurranse fra periode.
Data Frames brukes hovedsaklig for transmisjon av data under Konkurranse Perioden, og kan kombineres med pollling og acknowledgements i konkurranse fri modus.
Tegningen viser et standard IEEE 802.11 ramme format.
(Merk:
Frame body er variabel. Dette hvis er hvis en Wireless equivalent privacy (WEP) protokoll er implementert.
Duration field er en viktig del av koordineringsprotokollene. Forteller bl.a. Hvor lenge mediet vil bli opptatt ved sending av en ramme.
Hver addresse er en 48-bit MAC-addresse. Grunnen til så mange addresse-felt er at man bl.a. angir sender, mottaker, hvilke AP man vil sende gjennom eller til.
Type bitet forteller om det er en managament, kontroll eller data ramme.
(Noe av innholdet i rammen vil bli mer klart etter at vi har vist hvordan koordineringsprotokollene fungerer))

## Slide 34: Hidden Terminal Problem
Data
C may corrupt the
transmission between
A and B.
Hidden Terminal Problem!
A
B
C
D
Data
D will not transmit
Notes: Explain the interference range, there could be a node farther out which can interfere with B but cannot hear it. But still…

## Slide 35: CSMA/CA
Carrier Sense Multiple Access with Collision Avoidence (CSMA/CA)
  Listen before talking
RTS - Request To Send
CTS - Clear To Send
Notes: I WLAN brukes en Multipple aksess-metode som kalles CSMA/CA
Carrier sense beskriver det at senderen må lytte til mediet, etter bære-bølger, før man sender.
  dvs. prøver å detektere et signal fra en annen stasjon før man sender
  Hvis han oppdager et signal, venter han med å sende
Multiple Access beskriver det at flere noder prøver å sende på mediet samtidig
  Informasjon sendt fra en node blir mottatt av alle nodene innenfor dens rekkevidde.
The hidden terminal problem løses ved å innføre to nye meldinger
RTS er et en kort melding som sendes før dataene blir sendt. Denne spør om lov til å sende.
CTS er et svar fra mottaker om at sender nå kan begynne transmisjon av dataene.
  Disse meldingene vil da inneholde
    sender addressen,
    mottaker addressen og
    pakke størrelsen på dataene som skal sendes.
CSMA/CD kan ikke brukes fordi stasjonen ikke KAN lytte etter kollisjoner på kanalen samtidig som man sender.

## Slide 36: CSMA/CA (2)
ACK
CTS
Data
C will not
transmit to B.
Hidden Terminal Problem Solved
through RTS-CTS exchange!
A
B
C
D
RTS
D will not transmit
Notes: Her er det enorme gevinster å hente, fordi en stasjon ville ha fortsatt å sende hele PDUen uten å oppdage at en kollisjon hadde ødelagt hele transmisjonen. Grunnen til gevinst er at RTS og CTS er veldig små rammer.

## Slide 37: Two different MAC schemes
Distributed coordination function – DCF
  Best-effort
  Designed for asynchronous data transport
    All users have same chance of accessing the network
Point coordination function – PCF
  Optional
  Based on polling by an access point
  Designed for time-bounded traffic
Notes: På mac laget har vi to koordineringsfunksjoner.
Den første DCF er påkrevd. Dvs. at alle stasjoner må støtte denne koordinering-funksjonen.
Så det er den fundamentale aksesseringsmetoden for å støtte asynkon data overføring med best-effort.
Altså på en best mulig måte.
PCF er valgfri. Den baseres på polling fra et aksess-punkt. Den brukes som regel i kommunikasjon som stiller krav til tid.
PCF er påkrevd for contention frie perioder, mens DCF er basis ved contention periods.
Her ser vi en illustrasjon av hvordan PCF ligger over DCF på MAC laget.
DCF ligger rett over det fysiske laget.
DCF opererer da enten allene, eller sammen med PCF.

## Slide 38: MAC Access Modes
Distributed coordination function (DCF):
  CSMA/CA.
  DCF may use CTS/RTS to reduce the possibility of collisions.
Point coordination function (PCF):
  Contention-free services. Special stations called point coordinators are used to ensure contention-free.
  The coordinators reside in AP.
  PCF is only for infrastructure mode and not widely implemented.

## Slide 39: Distributed Coordination Function (DCF)
Used for contention services (CP)
Operates in ad-hoc networks
Operates either solely or coexist with PCF in infrastructure networks
Based on CSMA/CA
Uses RTS and CTS
Network Allocation Vector (NAV)
  A timer that indicates the amount of time the medium is to be reserved
  Each stations sets their NAV timer when a frame with a duration field is received
Notes: Brukes der stasjoner konkurerer om å få tilgang til mediet.
I ad-hoc nettverk operer den alene, mens den enten brukes alene, eller sammen med PCF i infrastruktur nettverk (nettverk som snakker med et AP).
DCF baserer seg på CSMA/CA, og RTS og CTS blir brukt.
Snakker gjerna om physical carrier sensing og virtual carrier sensing
PHYSICAL – en bruker observerer andre WLAN brukere ved å analysere deres pakker. Og at man oppdager aktivitet på kanalen ved å registrere signalstyrke fra andre kilder.
VÌRTUAL carrier sensing gjøres ved å sende varighet for en data enhet i duration feltet i rammene til RTS og CTS.
NAV: Brukes til å reservere mediet for en bestemt periode. En teller som indikerer hvor lenge mediet er opptatt.
  Hver stasjon oppdaterer telleren i vektoren når de mottar en ramme som inneholder et duration felt.
  I løpet av denn perioden vil ingen av stasjonen sende. Når telleren da når null vil mediet være ledig, og stasjoner kan begynne å konkurrere om tilgang til mediet.

## Slide 40: Virtual Carrier Sense
Used “Network Allocation Vector” (NAV)
  A timer for channel reserved period
  Included in the RTS and CTS frames
  Each station will count down until NAV = 0
  If NAV ≠ 0  Medium is Busy
  If NAV = 0  Medium is idle
The data frame has the ‘duration’ field, which indicates for how long the sender wants to hold the medium
Other stations read this field, and adjust a parameter called ‘Network Allocation Vector’ (NAV)
NAV indicates the amount of time that must elapse until the channel can be sampled again for idle status
NAV value thus indirectly indicates if the channel is free at any given time
  Using NAV value to determine channel status is called as ‘Virtual Carrier Sensing’

## Slide 41: Virtual Carrier Sense
A
B
Y
RTS
NAV set
CTS
Data(Z)
A
SIFS
SIFS
SIFS
Medium Idle
Medium Busy

## Slide 42: Access Spacing
Data
SIFS
PIFS
DIFS
time
IFS | Interframe Space |  | 
SIFS | Short IFS | Highest priority | ACK, CTS, 2nd MSDU
PIFS | PCF IFS | 2nd priority | PCF operation mode
DIFS | DCF IFS | 3rd priority | DCF operation mode
EIFS | Extended IFS | Lowest priority | Waiting period

## Slide 43: Backoff algorithm
data
wait
B1 = 5
B2 = 15
B1 = 25
B2 = 20
data
wait
B1 and B2 are backoff intervals
at nodes 1 and 2
cw = 31
B2 = 10
Notes: Vi har to noder. Node 1 med backoff interval B1 og node 2 med backoff interval B2.
Contention window er i dette eksemplet 31.
Nodene får så et tilfeldig backoff interval
  Node 1 B1=25
  Node 2 B2=20
Node2 har kortest interval, vinner og får da sende først.
  Når den har sendt ferdig velger den et nytt backoff interval, B2=15
Node1 har nå bare 5 time-slots igjen av backoffintervalet, og får da sende etter 5 time-slots.
Etter dette er Node1 ferdig, og Node2 kjører når backoff-intervallet dens er nedtelt.

## Slide 44: DCF Backoff
Similar to Ethernet
Collision is detected through a lack of ACK
If collision occurs, the station backs-off again; the mean of the back-off time is now doubled
Each retry
  window size increases
For DSSS
  Contention window = 2n – 1
  Smallest = 31, Biggest = 1023
DIFS
…
Window = 63 slots
#1 retry
DIFS
…
Max: Window = 1023 slots
#6 retry
DIFS
…
Min: Window = 31 slots
Start
…

## Slide 45: Sending Data and Ack
Ack
Data
Next MPDU
Source
Destination
Other
Contention Window
Defer Access
Backoff after Defer
DIFS
SIFS
DIFS
From WaveLAN Slide

## Slide 46: PCF operation
PC
Y
Z
NAV
Busy
Data(Z)
A
B
Data(Y)
A
Poll(Z)
End
NAV set
PIFS
A Point Coordinator (PC), located in the Access Point (AP) controls the PCF

## Slide 47: The coexist of DCF & PCF
B
PCF
DCF
CFP Repetition Interval
CFP
CP
B
PCF
DCF
CFP Repetition Interval
CFP
CP
A Point Coordinator (PC) resides in the Access Point and controls frame transfers during a Contention Free Period (CFP)
The CFP alternates with a Contention Period (CP) in which data transfers happen as per the rules of DCF

## Slide 48: Orthogonal Frequency Division Multiple Access (OFDMA)
Multicarrier Spread Spectrum Technique
High-rate serial data stream divided into numerous parallel low-rate data streams that are modulated by a set of subcarriers
Subacarriers are orthogonal with overlapping spectra
Pilot subcarriers for channel estimation

## Slide 49: Take advantage of OFDMA