## Slide 1: EMBEDDED Systems RELIABILITY
Lecture 1: fault modelling
Dimitrios agiakatsikas, Mihalis Psarakis

## Slide 2: Course outline
Lecture 1: Fault modelling. Defect-Faults-Errors-Failures. Fault models: stuck-at faults, stuck-open faults. Soft Errors. Single Event Effects (SEEs), SEUs, SETs, SEUs in FPGAs
Lecture 2: Reliability analysis, Fault injection experiments, Fault emulation, Radiation experiments, HW/SW benchmarks
Lab 1: Fault injection in FPGAs – Platform and experiments in simple circuits
Lab 2: Fault injection in FPGAs continue – Experiments in RISC-V
Lecture 3: Hardware fault tolerance. HW Redundancy (DMR, TMR, Diversified TMR, various TMR modes, local, global, distributed), Memory Scrubbing
Lecture 4: Fault tolerance for embedded microprocessors. SIHFT, Lockstep, checkpointing, watchdog timers
Lab 3: TMR in FPGAs
Lecture 5: Error Correction Codes
Lab 4: ECC in BRAMs
Lab 5: Safe FSM

## Slide 3: Dependability TREE
DEPENDABILITY
ATTRIBUTES
MEANS
IMPAIRMENTS
Reliability
Availability
Maintainability
Safety
Security
Testability
Fault Prevention
Fault Tolerance
Fault Removal
Fault Forecasting
Defects
Faults
Errors
Failures

## Slide 4: Impairments
Faults
  Physical change → Physical world
  Representation of a defect at the abstracted functional level
Errors
  Result of the fault → World of information
  The manifestation of the fault in the form of transmission of some erroneous information
Failures
  Deviation from desired service → External world
  When the provided service deviates from the predefined service – it is the result of the error
Physical
World
Informational
World
External
World
Faults
Errors
Failures
  Three worlds model

## Slide 5: Faults classification
Faults
Permanent
material defects, wearout
Temporary
Transient
Intermittent operation margins, infant mortality, process variation
Radiation soft errors
Non-radiation
power supply, EMI

## Slide 6: COMMON permanent Fault Models
Single stuck-at faults
Transistor open and short faults
Delay faults
.. They can be also used to model intermittent phenomena

## Slide 7: Number of faults
A given fault model has k types of faults
  k = 2 for most fault models
A given circuit has n possible fault sites
Multiple fault model –circuit can have multiple faults (including single faults)
  Number of multiple fault = (k+1)n-1
    Each fault site can have 1-of-k fault types or be fault-free
    The “-1” represents the fault-free circuit
  Impractical for anything but very small circuits
Single fault model – circuit has only 1 fault
  Number of single faults = k×n

## Slide 8: Single Stuck-at Fault
Three properties define a single stuck-at fault
    Only one line is faulty
    The faulty line is permanently set to 0 or 1
    The fault can be at an input or output of a gate
Example: XOR circuit has 12 fault sites ( ) and 24 single stuck-at faults
a
b
c
d
e
f
1
0
g
h
i
1
s-a-0
j
k
z
0(1)
1(0)
1
Test vector for h s-a-0 fault
Good circuit value
Faulty circuit value

## Slide 9: Stuck-at Faults
x1
x2
x3
y
a
b
c
d
e
f
g
h
i
x1x2x3 | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
y | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
a SA0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
a SA1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1
b SA0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
b SA1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
c SA0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
c SA1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1
d SA0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
d SA1 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1
e SA0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
e SA1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
f SA0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
f SA1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
g SA0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
g SA1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
h SA0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
h SA1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
i SA0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
i SA1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Truth table for fault-free behavior
and behavior of all possible stuck-at faults
Any line can be
  Stuck-at-0 (SA0)
  Stuck-at-1 (SA1)
    # fault types: k=2
Example circuit:
  # fault sites: n=9
  # single faults =2×9=18

## Slide 10: Stuck-at Faults
x1x2x3 | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
y | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
a SA0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
a SA1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1
b SA0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
b SA1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
c SA0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
c SA1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1
d SA0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
d SA1 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1
e SA0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
e SA1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
f SA0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
f SA1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
g SA0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
g SA1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
h SA0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
h SA1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
i SA0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
i SA1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Truth table for fault-free behavior
and behavior of all possible stuck-at faults
Valid test vectors
  Faulty circuit differs from good circuit
  Necessary vectors:
    011 detects f SA1, e SA0
    100 detects d SA1
    Detect total of 10 faults
    001 and 110 detect remaining 8 faults
x1
x2
x3
y
a
b
c
d
e
f
g
h
i

## Slide 11: Transistor Faults
VDD
VSS
B
P1
P2
N2
N1
A
Z
2-input
CMOS
NOR
gate
Any transistor can be
  Stuck-short
    Also known as stuck-on
  Stuck-open
    Also known as stuck-off
    # fault types: k=2
Example circuit
  # fault sites: n=4
  # single faults =2×4=8

## Slide 12: Transistor Faults
VDD
VSS
B
P1
P2
N2
N1
A
Z
2-input
CMOS
NOR
gate
Stuck-short faults cause conducting path from VDD to VSS
  Can be detect by monitoring steady-state power supply current IDDQ
Stuck-open faults cause output node to store last voltage level
  Requires sequence of 2 vectors for detection
    0010 detects N1 stuck-open

## Slide 13: Stuck-Open Example
Two-vector stuck-open test
can be constructed by
ordering two stuck-at tests
A
B
VDD
C
pMOS
FETs
nMOS
FETs
Stuck-
open
1
0
0
0
0
1(Z)
Good circuit states
Faulty circuit states
Vector 1: test for A s-a-0
(Initialization vector)
Vector 2 (test for A s-a-1)

## Slide 14: Stuck-Short Example
A
B
VDD
C
pMOS
FETs
nMOS
FETs
Stuck-
short
1
0
0 (X)
Good circuit state
Faulty circuit state
Test vector for A s-a-0
IDDQ path in
faulty circuit

## Slide 15: Transistor Faults
AB | 00 | 01 | 10 | 11
Z | 1 | 0 | 0 | 0
N1 stuck-open | 1 | 0 | last Z | 0
N1 stuck-short | IDDQ | 0 | 0 | 0
N2 stuck-open | 1 | last Z | 0 | 0
N2 stuck-short | IDDQ | 0 | 0 | 0
P1 stuck-open | last Z | 0 | 0 | 0
P1 stuck-short | 1 | 0 | IDDQ | 0
P2 stuck-open | last Z | 0 | 0 | 0
P2 stuck-short | 1 | IDDQ | 0 | 0
VDD
VSS
B
P1
P2
N2
N1
A
Z
2-input
CMOS
NOR
gate
Truth table for fault-free circuit
and all possible transistor faults

## Slide 16: Delay Faults
0 0 x1
0 1 x2
v2 v1
1 1 x3
y
2
3
3
2
t=0
t=2
t=7
Path-delay fault model considers cumulative propagation delay through CUT
  2 test vectors create transition along path
  Faulty circuit has excessive delay

## Slide 17: Pattern Sensitivity and Coupling Faults
Common in high density RAMs
Pattern sensitivity fault
  Contents of memory cell is affected by contents of neighboring cells
Coupling fault
  Transition in contents of one memory cell causes change in contents of another cell
Detected with specific memory test algorithms
  March test algorithm
Test Algorithm | March Test Sequence
March | ↨(w0); ↓(r0, w1); ↑(r1, w0, r0, r0, w1); ↑(r1, w0); ↑(r0, w1, r1, r1, w0); ↑(r0)
Notation:
w0 = write 0 (or all 0’s)
r1 = read 1 (or all 1’s)
↑= address up
↓= address down
↨ = address either way

## Slide 18: soft errors
The result of a transient fault that corrupts system data but does not cause any hardware damage
After the appearance of the soft error the system will have the same reliability
It is also called Single Event Upset (SEU)
0
1

## Slide 19: Soft error: Known Case 1
A satellite was launched from the Baikonor Cosmodrome (Kazakhstan, May 31, 2005)
It crashed during the 5th orbit, having to perform 253 orbits
Possible cause: soft error in SRAM
Source: Reno Harboe-Sψrensen, ESA-ESTEC, ” Radiation Effects in Spacecraft Electronics“, 5th LHC Radiation Workshop –Nov-29, 2005.

## Slide 20: Soft error: known case 2
Electronic voting elections (Belgium, 05/18/2003)
An error was detected in the city of Schaerbeek:
  More votes than the registered voters
  4096 votes … more
  Unable to validate the results ...
Possible cause: soft error in the 13th bit of a word in SRAM
Source: Expert board report – Elections on 05/18/2003

## Slide 21: Radiation Effect on CMOS ICs
Impact by high-energy particles, such as protons or heavy ions
From: http://ajnoyola.com/RHBD_primer.html
Radiation ionizes the oxide, creating electrons and holes; the electrons then flow out, creating a positive charge which leads to current leak across the channel
Single Event Transient (SET): A current pulse occurring at a circuit node due to single energetic particle event
Single Event Upset (SEU): A change in a circuit’s logic state induced by a single energetic particle event
Time
Transient
Current Pulse
Single Event Effects (SEEs)
Notes: Explanation from: Patel-Predd, P., “Transistors in Space: NASA Tests New Radiation-Proof Chips,” IEEE Spectrum, Vol. 45, No. 8, p. 17, August 2008.

## Slide 22: Radiation environment

## Slide 23: WHAT DO soft errors AFFECT?
Memories (caches, SRAM, DRAM)
  Flip the memory bit
Registers (flip-flops)
  May affect the outcome of an instruction due to a bit flip in a pipeline register
Combinational logic (logic gates)
  May affect the outcome of an operation due to a single event transient (SET) in the datapath
Combinational Logic
Flip-
flops
Memory
Source: Public
Soft Error rate contributions
(Enterprise networking chip)

## Slide 24: Strike on state bit (e.g., in register file)
Bit
Read
Bit has error protection
Error
is only detected
(e.g., parity +
no recovery)
Error can be
corrected
(e.g, ECC)
yes
no
Does bit matter?
Silent Data Corruption (SDC)
yes
yes
no
Detected, but unrecoverable error (DUE)
no error
yes
no
benign fault
no error
benign fault
no error
Notes: Transition: Based on this figure, here are our definitions …
Talk about “Does bit matter” as a forward pointer for ACE later
Bit flip in quicksort … often doesn’t matter!

## Slide 25: Does a SET always cause a soft error?
Single Event Transient (SET)
Registers
Registers
0
1
0
1
0
1
1
1
0
1
1
1
logical masking
electrical masking

## Slide 26: Does a SET always cause a soft error?
Latch window masking
setup
time
hold
time
clock
data
data
data
SET will be propagated
SETs will not be propagated

## Slide 27: soft error rates
Error rates are commonly measured using:
  MTΒF (Mean Time Between Failures) ή MTTF
For the soft errors we use:
  FIT (Failure in Time) = 1 failure in 109 hours
  1 year MTBF = 109/(24*365) FIT ~ 114Κ FIT
Soft error rate depends on scaling and altitude

## Slide 28: Field Programmable Gate Arrays
Configuration
Logic Block
(CLB)
Block RAM
Multipliers
Programmable I/Os
Digital Clock Manager

## Slide 29: Soft errors IN FPGAs
The problem of radiation-induced SEEs is bigger in FPGAs!
  FPGAs relies in SRAM to configure the combinational logic and the interconnection
  The effect of SEUs in the configuration bits is persistent

## Slide 30: SEU in FPGA
source: actel

## Slide 31: SEU in FPGA: routing
GRM: General Routing Matrix

## Slide 32: SEU in FPGA: function
Source: Semico 2002

## Slide 33: SOFT ERROR RATE in TERRESTRIAL applications
Similar to Xilinx Device Reliability Report (UG116 (v10.14) April 23, 2021)
Data from LANSCE Neutron
Memory | Fluence (n/cm2) | SEUs | Cross section per device [cm2] | Cross section per bit [cm2/bit]
CRAM | 1.202E+11 | 2417 | 2.01 x 10-8 | 1.84 x 10-16
BRAM | 1.202E+11 | 10118 | 8.42 x 10-8 | 1.21 x 10-15
SEU rate per device = cross section per device x flux (at NYC level 13 n/cm2/h)
For CRAM: 262 FIT per device OR 1 soft error per 436 years
Xilinx UltraScale+ device

## Slide 34: SOFT ERROR RATE in space applications
Category | In-flare rate |  |  | Out-of-flare rate |  | 
 | Heavy ions | Protons | Total | Heavy ions | Protons | Total
PL - CRAM SEUs | 1.50e+02 | 1.60e+02 | 310 | 2.19e-01 | 3.03e+00 | 3.24
Xilinx Zynq-7000 device
Predicted error rates (soft errors/device/day) for the Low Earth Orbit (LEO) (800 km, 98.0° inclination)